## Slide 1
Design and Simulation of a 16-Bit Computer Using Logisim Evolution
Presented by: Ahmad Rayan Qasim, Abdul Kabir Syed, Attique Alvi, Abdul Samad
Course: EE123 - Digital Logic Design
Supervisor: Prof. Mughees Ahmad
Submission Date: 17 June 2025

## Slide 2
Project Overview
Objective
Build a 16-bit computer from basic components.
Tool
Logisim Evolution for simulation.
Method
Designing from scratch, no pre-made CPUs.
Focus
Instruction cycle, data processing, control flow.

## Slide 3
Main Components
ALU
Arithmetic and logical operations.
Registers
Temporary data storage.
RAM
Stores instructions and data.
Program Counter
Points to next instruction.
Control Unit
Directs CPU operations.
Clock
Synchronizes all operations.

## Slide 4
Additional Components (New Additions)
Instruction Register (IR)
Holds current fetched instruction.
Flags Register
Stores status flags (Z, C, N, V).
Stack Pointer (SP)
Points to stack top for calls/state.
MAR
Memory Address Register for R/W.
MUX
Directs signals between components.

## Slide 5
How the Instruction Cycle Works
Fetch
PC sends address to RAM; instruction to IR.
Decode
Control Unit interprets instruction.
Execute
ALU/data path components carry out.
Store
Result saved in Register or RAM.
PC Increments
Points to next instruction.

## Slide 6
ALU and Flag Register
ALU Capabilities
Add, Subtract
AND, OR, NOT, XOR
Outputs: Result + Flag signals
Flag Register
Zero (Z)
Carry (C)
Negative (N)
Overflow (V)
Used for conditional branching

## Slide 7
Control Unit & Microoperations
Control Unit
Decodes instruction opcode. Triggers micro-operations.
Micro-operations
Enable Register → ALU. Write RAM → Register. PC + 1 → PC.

## Slide 8
Memory & Stack Operations
1
RAM
Stores programs and data. Addressed by MAR, via data bus.
2
Stack
Push/Pop operations via SP. Supports subroutines.

## Slide 9
Simulation & Results
1
Test Programs
Addition, Subtraction, Comparison. Register ↔ RAM data transfer.
2
Instruction Cycle
Observed in real time.
3
ALU Accuracy
Accurate logic/arithmetic.
4
Synchronization
All components worked synchronously via Clock.

## Slide 10
Conclusion & Future Work
Conclusion
Functional simulated 16-bit computer
Hands-on learning of hardware concepts
Future Enhancements
Add I/O devices (Keyboard, Display)
Implement Interrupts & System Calls
Expand instruction set
Create graphical assembler/interface